## Slide 1
PATENT LANDSCAPE · TECHNOLOGY · WHITESPACE · COMPETITION
AR Glasses & Head-Mounted
Display Patents
A landscape for inventors — where invention is happening, where the white space is, and what to build next. Scope spans every head-worn device: optical see-through AR / smart glasses, mixed-reality and VR headsets.
140,000+
patents in the universe
67,000+
INPADOC families
40+
patent records examined
20+
startups profiled
Synthesized from IPlytics / LexisNexis, GlobalData, Vitek IP, Finnegan, PatSnap, academic patent studies & primary patent records · Data through Q2 2026

## Slide 2
HOW TO READ THIS DECK
Methodology, scope & how many patents were read
Scope — “AR glasses” = every head-mounted device
Optical see-through AR / smart glasses (waveguide & birdbath)
Mixed-reality headsets — Apple Vision Pro, HoloLens, Galaxy XR
VR headsets — Meta Quest, PSVR, Varjo
Audio / camera “AI glasses” — Ray-Ban Meta, Oakley HSTN
Enabling subsystems — optics, displays, sensors, input, silicon, EMG
How many patents were read
40+
individual patents & published applications examined directly — abstracts, claims, assignee/priority data verified on Google Patents & USPTO
10
foundational patents read in depth and mapped to today’s products
140,000+
patents / 67,000+ families covered through synthesized landscape datasets
Sources & a note on the numbers
Counts differ by methodology (keyword vs. CPC/IPC, family vs. document, jurisdiction) and by vendor, so figures from different firms are not strictly comparable; 2024–2026 totals are understated by the ~18-month publication lag. Where a chart is reconstructed from multiple sources it is marked “indicative.” Patent numbers prefixed US 20xx/… are published applications, not grants. Primary sources: IPlytics/LexisNexis, GlobalData, Vitek IP, Finnegan quarterly trackers, PatSnap, Sagacious IP, IFI Claims, IDC, and the patent records themselves.
2
AR / HMD PATENT LANDSCAPE

## Slide 3
EXECUTIVE SUMMARY
Six things an inventor needs to know
The field is large and still compounding
140k+ patents / 67k+ families and counting; granted AR patents grew ~82%/yr after 2012. The moat is concentrated in optics and input, not apps.
China now leads issuance volume
SIPO overtook the USPTO in Q4 2020 and held the lead through 2021. The US still dominates high-value families; Korea, GB & Japan follow.
Six holders own the core
Magic Leap, Microsoft, Sony, Samsung, LG, Apple, Meta & Google dominate. Magic Leap is the only pure-play in the top tier; Apple’s spatial portfolio is ~5,000 strong.
Display & optics is the battleground
Waveguides (diffractive, reflective, holographic) + microLED light engines absorb the most filings. Whoever solves bright, wide-FOV, slim optics wins.
White space is in the hard physics
Hard-edge occlusion, vergence-accommodation conflict, all-day thermal/power, and prescription-integrated optics are unsolved — the richest invention targets.
Input just shifted to the wrist
Meta’s sEMG Neural Band (Sept 2025) opened a new neural-input layer it now leads with ~238 patents — alternative biosignal input is open territory.
3
AR / HMD PATENT LANDSCAPE

## Slide 4
WHY THE PATENTING IS ACCELERATING
Market context: the demand pulling the IP
AR/VR market revenue (USD bn)
Chart: 
| 2022 | 2027F
USD bn | 37 | 114.5
↑ ~25.3% CAGR 2022–2027 (industry consensus)
Smart-glasses unit shipments (millions)
Chart: 
| H1'25 | 2025 | 2026F | 2027F | 2028F | 2029F
Units (m) | 4.1 | 8 | 14.5 | 22 | 31 | 40
IDC: H1'25 shipments +64% YoY; China the fastest market at ~56% CAGR
$114.5bn
projected AR/VR market by 2027
>40m
smart-glasses units/yr forecast by 2029
~66%
of the VR-device market is head-mounted displays
14.3m
AR/VR headsets shipping in 2025 (IDC)
Market figures: MarketsandMarkets / industry consensus; shipment data: IDC Worldwide AR/VR & smart-glasses trackers (2025). Forecast years indicative.
4
AR / HMD PATENT LANDSCAPE

## Slide 5
THE SHAPE OF THE CURVE
Patent filings: a decade of compounding growth
Indicative AR/VR/HMD patent publications per year
Chart: 
| 2012 | 2014 | 2016 | 2018 | 2020 | 2022 | 2024
Publications | 1200 | 3200 | 6800 | 11000 | 13500 | 12800 | 11500
Indicative reconstruction (IPlytics, Finnegan, academic data). Dip after 2022 reflects publication lag + re-coding of filings to AI classes — not a real decline.
~82%
annual growth in granted U.S. AR patents after 2012 (academic USPTO study)
2×
filings roughly doubled every ~4 years through 2018 (IPlytics)
Q4 2020
China’s SIPO overtakes the USPTO in AR/VR issuance — and never looks back
~2,700
AR/VR patents granted worldwide in a single quarter (Q3 2021)
Trend chart is an indicative synthesis across sources; absolute yearly counts vary by database and search definition.
5
AR / HMD PATENT LANDSCAPE

## Slide 6
WHERE IT IS BEING FILED
Geographic distribution of AR/VR patents
AR/VR patents granted by office — Q4 2021 snapshot
Chart: 
| China (SIPO) | United States | South Korea | Great Britain | Japan
Patents granted | 1164 | 725 | 261 | 126 | 115
The center of gravity is moving east
Historically >55% of AR/VR filings originated in the U.S. (IPlytics) — still the venue with the highest-value families.
China leads raw issuance volume since Q4 2020 and is the fastest-growing market (~56% CAGR), backed by a deep supply chain: BOE, Goertek, JBD, Sunny Optical.
Korea (Samsung, LG) and Japan (Sony) anchor display & sensor IP.
Inventor takeaway: file in US + CN + KR + JP + EP; a US-only filing leaves the fastest-growing market open.
Snapshot: Finnegan AR/VR Patent Prosecution Update, Q4 2021 (patents granted, by office). Historical filing share: LexisNexis IPlytics.
6
AR / HMD PATENT LANDSCAPE

## Slide 7
WHO OWNS THE CORE
Top patent holders & portfolio scale
Largest AR/VR portfolios, 2002–2022 (patents published)
Chart: 
| Magic Leap | Microsoft | Sony | Samsung | LG
Patents | 3786 | 3647 | 3612 | 1749 | 1556
Top 5 together held ~14,350 AR/VR patents (GlobalData, TMT sector).
2023 top assignees (Vitek IP)
Magic Leap · Microsoft · Samsung · Google · Meta
Qualcomm · LG · IBM · Sony · BOE Technology
Apple’s spatial-computing estate is ~5,000 patents; Meta filed ~5,000 tied to its programs.
One number to remember
Snap holds 200+ pending AR/VR applications — more than any other company — a leading indicator of where a future portfolio leader is forming.
Portfolio counts: GlobalData (TMT, 2002–2022) & Vitek IP 2023 AR/VR Patent Market Overview. Apple/Meta spatial estimates from public analyses; methodologies differ.
7
AR / HMD PATENT LANDSCAPE

## Slide 8
HOW THE LEADERS PLAY
IP strategy: build, buy, and pure-play bets
Pure-play vs. platform
Magic Leap is the only top-tier holder built solely on AR — ~3,800 patents, yet it pledged ~1,903 of them to JPMorgan Chase as loan collateral (2019).
Big-tech holders (Microsoft, Sony, Samsung, Apple) fund AR from vast cross-domain portfolios — they can out-wait pure-plays.
Growth by acquisition
Meta bought Oculus (2014), CTRL-labs (2019, ~$0.5–1bn) for EMG, and gained Orion optics know-how.
Snap acquired WaveOptics (waveguides) to power Spectacles.
Microsoft absorbed Osterhout/ODG-era IP; China’s Crystal-Optech took a stake in Israel’s Lumus.
What it means for you
Foundational optics IP is concentrated and partly tradeable — licensing and acquisition are realistic routes.
A focused, defensible cluster (10–30 strong claims in a white-space niche) is an acquisition magnet, exactly the Oculus/CTRL-labs/WaveOptics pattern.
Magic Leap collateral pledge: UCC filing reporting; acquisition figures from public reporting (CTRL-labs estimate $0.5–1bn).
8
AR / HMD PATENT LANDSCAPE

## Slide 9
THE MAP OF INNOVATION
Technology taxonomy: where invention is happening
Filing intensity by technical cluster — darker = more crowded
Very high
High
Moderate
Emerging / open
Waveguides & combiners
Diffractive (SRG), reflective/geometric, holographic, metasurface, SiC substrates
Light engines / micro-displays
microLED (LEDoS), LCoS, micro-OLED, laser beam scanning, birdbath
Eye tracking & foveation
Waveguide-integrated IR gaze, foveated rendering, IPD calibration
Hand tracking & gesture
Optical hand pose, controllers, surface touch typing
Neural / EMG input
sEMG wrist (Meta Neural Band), biosignal interfaces — newly opened
SLAM & spatial computing
World mapping, persistent anchors, plane detection, relocalization
Silicon / SoC & compute
Snapdragon XR2+/AR1, custom spatial chips, split-compute pucks
Power & thermal
Energy density, hot-swap/structural batteries, thermal dissipation — open
Brightness & efficiency
Outdoor nits, waveguide efficiency, eye-glow suppression — open
Vergence-accommodation / depth
Varifocal, multi-focal, light-field, holographic — largely open
Audio
Open-ear speakers, bone conduction, gaze-directed / private audio
On-device & multimodal AI
Assistants (Meta AI, Gemini, Qwen), scene understanding, translation
Intensity is a qualitative synthesis of filing activity across landscape reports — not a precise per-class count.
9
AR / HMD PATENT LANDSCAPE

## Slide 10
DEEP DIVE 1 OF 3
Display & optics — the battleground
Waveguide combiner families
Diffractive (SRG)
Microsoft, Snap/WaveOptics, Dispelix, Vuzix — slim, scalable, but limited efficiency & “eye-glow.”
Reflective / geometric
Lumus (US 7,457,040) — partial-mirror array; brighter & color-true, harder to mass-produce.
Holographic / Bragg
DigiLens (US 9,933,684) switchable Bragg gratings; volume holograms.
Silicon-carbide
Meta Orion (US 2024/0179284) — high refractive index enables ~70° FOV from a single plate.
Light engines / micro-displays
microLED (LEDoS)
JBD, Mojo Vision, Saphlux, Porotech — highest brightness/efficiency at tiny size; full-color single-panel is the prize.
LCoS
Avegant, Raontech, Omnivision — mature, compact, used in light glasses.
micro-OLED
Sony — deep blacks; powers Vision Pro & Galaxy XR (dual 3,552×3,840).
Laser beam scanning
Microvision (US 7,061,450) — RGB MEMS; HoloLens 2 engine.
Birdbath / flat-prism
XREAL, Brilliant Labs — cheap, wide FOV, but bulkier than waveguides.
Architectures and exemplar assignees compiled from patent records and supply-chain analyses (TrendForce, KGOnTech).
10
AR / HMD PATENT LANDSCAPE

## Slide 11
DEEP DIVE 2 OF 3
Input & interaction — the shift to the wrist
Eye tracking & gaze
Waveguide-integrated IR tracking (Microsoft US 9,759,913 / 9,759,917).
Enables foveated rendering (render sharp only where you look) — a power lever.
Apple uses gaze as the primary Vision Pro pointer; IPD auto-calibration.
Hand & gesture
Optical hand-pose tracking on Quest & Vision Pro — but fails when hands leave the camera view or in low light.
Controllers persist for precision & haptics in VR/gaming.
Neural / EMG (new)
Meta Neural Band (Sept 2025): surface-EMG wrist reads motor signals before motion is visible; ~238 CTRL-labs patents.
Works hands-down, in the dark, in public; ~200k research participants; on-device decode.
Rivals: Mudra Link ($199) — alternative biosignal input is open.
Inventor signal: input is the second moat after optics. Meta has locked the wrist-EMG lane; calibration-free generalization, non-wrist biosignals, sub-$50 EMG, and haptic-confirmed micro-gestures remain open and acquisition-friendly.
Patent identifiers verified on Google Patents/USPTO; Neural Band detail from Meta & Nature 2025 (Kaifosh & Reardon, sEMG neuromotor interface).
11
AR / HMD PATENT LANDSCAPE

## Slide 12
DEEP DIVE 3 OF 3
Spatial computing, sensing & on-device AI
SLAM & world understanding
Environment mapping & relocalization (Microsoft US 9,467,920); plane detection; persistent shared anchors.
The substrate for stable holograms and multi-user AR — crowded, but quality still varies.
Silicon & compute topology
Qualcomm Snapdragon XR2+/AR1 dominate; XREAL ships a custom X1S spatial chip.
Split-compute (glasses + phone/puck) trades latency & heat for battery — an active design axis.
On-device & multimodal AI
The assistant is becoming the product: Meta AI, Gemini (Android XR), Alibaba Qwen run scene understanding, translation, step-by-step guidance.
AI-native “camera glasses” (Ray-Ban Meta) outsell display glasses today — a viable wedge with no waveguide at all.
Audio & ambient sensing
Open-ear & bone-conduction audio; gaze-directed private sound.
Always-on cameras/mics raise privacy & power questions — see white-space.
12
AR / HMD PATENT LANDSCAPE

## Slide 13
THE BEDROCK
Top 10 foundational patents — what shaped AR top to bottom
# | Patent | Assignee | What it covers · why it is foundational
1 | US 5,467,104 | Univ. of Washington | Virtual retinal display — scans light directly onto the retina; root of all retinal-projection near-eye displays.
2 | US 7,457,040 | Lumus | Light-guide optical device (LOE) — partial-mirror reflective waveguide; reference architecture for reflective combiners.
3 | US 9,063,330 | Oculus / Meta | Predictive head tracking — forecasts motion to cut latency & judder; made consumer VR comfortable.
4 | US 9,372,347 | Microsoft | Diffractive waveguide — in-couple → fold/exit gratings for pupil expansion; the HoloLens optical blueprint.
5 | US 9,791,700 | Magic Leap | Stacked-waveguide light field — multiple depth planes via DOEs to attack vergence-accommodation conflict.
6 | US 9,285,589 | Osterhout / ODG | See-through head-worn computer — broad early smart-glasses systems IP that fed Microsoft & the industry.
7 | US 10,203,489 | Apple | HMD optical system — anchors the Vision Pro pancake-optics continuation family.
8 | US 9,933,684 | DigiLens / SBG | Switchable Bragg-grating waveguide — electrically switchable holographic gratings (HPDLC).
9 | US 7,061,450 | Microvision | Scanned-beam display — RGB laser MEMS retinal scanning; behind the HoloLens 2 laser engine.
10 | US 8,294,994 | Google | Non-parallel-surface image waveguide — Google Glass-era near-eye HUD optics.
Patent numbers, assignees & priority data verified on Google Patents/USPTO. “Foundational” reflects architectural influence & forward citations, not a citation ranking.
13
AR / HMD PATENT LANDSCAPE

## Slide 14
THE LEADING EDGE
Recent & emerging patents (2023–2026)
Patent / family | Assignee | What it covers
US 2024/0179284 | Meta | Single double-sided silicon-carbide diffractive waveguide — enabled Orion’s ~70° FOV from one plate.
US 2025/0004275 | NVIDIA | Backlight-free AR via digital holography + U-Net neural net for per-pixel occlusion & selective dimming.
US 12,140,741 | Apple | Pancake optical system — Vision Pro family continuation.
US 11,815,685 | Apple | Adjustable virtual-image distance + corrective (prescription) lenses for an HMD.
US 12,085,721 | (Japan) | Optical-waveguide detection element — fuses eye-tracking + video light source into one waveguide for miniaturization.
US 10,838,110 | Microsoft | Metasurface optical coupling elements for display waveguides.
US D1,042,452 | Apple | Vision Pro head-mounted display — ornamental design patent.
238-patent family | Meta (CTRL-labs) | Surface-EMG neuromotor input — the IP basis of the Neural Band wrist controller.
189-patent family | Meta | Pancake-optics & varifocal stacks — thinner Quest Pro/Quest 3 headsets.
US 11,448,879 | Brilliant Labs | Open-source lightweight AR-glasses architecture (Frame).
What the 2024–26 wave tells you
New materials win FOV — silicon carbide is the breakout (Meta).
Occlusion & dimming go computational — holography + neural nets (NVIDIA).
Prescription correction is now patentable subject matter at the optics layer (Apple).
Sensor fusion into the waveguide drives miniaturization.
Input moved to the body — EMG is a fresh, defensible layer.
US 20xx/… are published applications, not grants. Family sizes (238 / 189) per PatSnap. Verify exact claim scope before relying on any single record.
14
AR / HMD PATENT LANDSCAPE

## Slide 15
THE CENTRAL CONSTRAINT
The “impossible triangle” of AR glasses
Wide FOV
immersion
Slim & light
all-day wear
Power & bright
battery + nits
Optimize
any two
Why it is the master problem
Every AR optical decision trades these three against each other. A slim waveguide loses FOV and efficiency; a wide-FOV birdbath gets bulky; pushing brightness through low-efficiency optics drains the battery and adds heat. No shipping product wins all three at once — that gap is the invention frontier.
Meta Orion
Wins FOV (70°) — needs SiC optics, a wireless compute puck & ~$10k build. Not for sale.
Ray-Ban Display
Wins slim & social — but a ~20° monocular HUD, 600×600. $799, ships now.
Quest 3 / Galaxy XR
Win capability & brightness — but bulky headsets, external/short battery.
15
AR / HMD PATENT LANDSCAPE

## Slide 16
WHAT IS STILL HARD
The biggest unsolved challenges
FOV vs. form factor
Hard
Slim waveguides cap near 50°; wide FOV needs bulk or exotic substrates (SiC).
Battery & thermal
Hard
Rendering + sensors + projection is power-hungry; all-day glasses need a step change in energy density.
Brightness outdoors
Improving
Need thousands of nits to the eye through low-efficiency (1–2%) waveguides.
Vergence-accommodation
Unsolved
Fixed focal plane causes eye strain/nausea; varifocal & light-field still immature.
Weight, comfort & stigma
Improving
Sub-50 g all-day comfort, plus the social cost of visible cameras (“glasshole”).
Cost & yield
Hard
Waveguides are expensive & low-yield; microLED full-color panels are not yet cheap at scale.
Plus two cross-cutting hard problems carried into white-space: hard-edge optical occlusion and motion-to-photon latency.
16
AR / HMD PATENT LANDSCAPE

## Slide 17
WHERE TO INVENT
The white-space map — crowding vs. impact
PATENT CROWDING →
open
crowded
COMMERCIAL IMPACT →
GO ZONE
Hard-edge occlusion
Compact varifocal / VAC
All-day thermal & power
Rx-integrated optics
Alt. neural / biosignal input
Privacy-preserving sensing
Eye-glow / WG efficiency
Full-color 1-panel microLED
Diffractive waveguides
SLAM / anchors
How to read it
Go zone (top-left): high impact, still-open IP — occlusion, varifocal/VAC, thermal & power, prescription optics, alternative input.
Top-right is high-impact but crowded — microLED & diffractive waveguides. Enter only with a sharp, novel sub-claim or a license.
Bottom-right (SLAM/anchors) is crowded and commoditizing — weakest ROI for a new filer.
Positions are an analyst assessment of relative crowding & commercial impact — a prioritization aid, not a measured coordinate.
17
AR / HMD PATENT LANDSCAPE

## Slide 18
THE SHORTLIST
Six white-space bets worth a patent program
1
Hard-edge optical occlusion
Make virtual objects truly block real light — per-pixel LC / electrochromic dimmers, occlusion-capable waveguides. Only NVIDIA’s holographic approach is early; field wide open.
2
Compact, low-power varifocal
Solve vergence-accommodation without bulk — LC lens stacks, metasurface focal control, single-layer focal-free optics. Meta leads pancake-varifocal; metasurface VAC is open.
3
All-day thermal & power
Energy-dense / structural batteries, sub-milliwatt display drive, smart compute-offload, motion-to-photon reduction. The gating constraint for true glasses.
4
Prescription-integrated optics
Vision correction co-designed with the combiner — adjustable / liquid-crystal Rx. Big-tech portfolios are thin here and it is consumer-critical (most adults need correction).
5
Alternative neural / biosignal input
Meta owns sEMG-wrist (238 patents). Open: calibration-free generalization, non-wrist biosignals, sub-$50 EMG, haptic-confirmed micro-gestures (cf. Mudra Link $199).
6
Privacy-preserving always-on sensing
On-device redaction, hardware capture indicators, consent signaling. A regulatory + patent gap as cameras/mics go always-on (GDPR friction).
18
AR / HMD PATENT LANDSCAPE

## Slide 19
WHO IS BUILDING
The startup & specialist ecosystem
Optics & display enablers
Lumus — reflective waveguides (supply Meta/Google per reports)
DigiLens — switchable Bragg-grating waveguides
WaveOptics — diffractive (acquired by Snap)
Avegant — tiny LCoS/LED light engines
Mojo Vision — high-density microLED panels
JBD / Saphlux / Porotech — microLED suppliers
Consumer AI / AR glasses
XREAL — birdbath; Google Android XR lead HW partner
Rokid — AI glasses; record XR crowdfund
Even Realities — ~43 g HUD, no camera, Rx-ready
Brilliant Labs — open-source Frame (~40 g)
RayNeo (TCL) · INMO · Thunderbird — China cohort
Enterprise & specialists
Magic Leap — waveguide mfg + Android XR pivot
Vuzix — diffractive + microLED, enterprise
Varjo — “human-eye” resolution MR for sim/enterprise
Tilt Five — tabletop AR gaming
Solos — smart eyewear; claims 100+ patents
XREAL
$433m raised · ~$1bn valuation
Rokid
$228m raised · ~$1bn · $4m crowdfund
Magic Leap
~3,800 patents · ~1,903 pledged to JPMorgan
Snap
200+ pending AR/VR applications
Funding & portfolio figures: Crunchbase, Bloomberg, PRNewswire, company statements (2025–26). Supply relationships per industry reporting.
19
AR / HMD PATENT LANDSCAPE

## Slide 20
PROBLEM → PLAYER
Who is solving what — and their IP signal
Player | Core technology | Problem it solves | IP / funding signal
XREAL | Birdbath / flat-prism micro-OLED | Wide-FOV AR at low cost, today | $433m raised; X1S chip; Android XR lead HW partner
Rokid | microLED waveguide + on-device AI | Lightweight (49 g) AI glasses with open SDK | $228m; record $4m XR crowdfund
Even Realities | Discreet monochrome HUD, no camera | Socially invisible glasses for text/translation | ~43 g; prescription-compatible
Lumus | Reflective (geometric) waveguides | Bright, color-true combiners | US 7,457,040; Crystal-Optech stake
DigiLens | Switchable Bragg-grating waveguides | Low-cost holographic waveguides | US 9,933,684; Mojo microLED partner
Mojo Vision | High-density red / RGB microLED | Brightness & efficiency at glasses scale | Pivoted from AR contact lens to panels
Magic Leap | Stacked diffractive waveguides | Depth-plane AR; waveguide manufacturing | ~3,800 patents; licensing & Android XR
Varjo | Dual-display “human-eye” resolution | Enterprise simulation & design fidelity | High-end MR; defense/industrial
Solos | Multimodal sensing + beamforming audio | Smart-eyewear sensing & private audio | Claims 100+ patents; suing Meta (2026)
Brilliant Labs | Open-source birdbath + AI | Hackable, developer-first AR glasses | US 11,448,879; ~40 g Frame
Technology focus & problem framing from product materials and patent filings; signals from public funding/IP disclosures.
20
AR / HMD PATENT LANDSCAPE

## Slide 21
THE CUTTING EDGE
New inventions emerging right now
Silicon-carbide single-layer waveguides
Meta Orion uses a high-index SiC plate + slant-etched gratings to hit ~70° FOV without the rainbow stray-light of stacked glass — a new materials frontier the supply chain is now chasing.
Backlight-free holographic occlusion
NVIDIA’s digital-holography stack (US 2025/0004275) uses a spatial light modulator + neural net to dim or occlude per-pixel — attacking occlusion and power at once.
Non-invasive neuromotor input
Meta’s sEMG Neural Band reads motor intent at the wrist (Nature 2025) — input without cameras, in the dark, in public. The first mainstream neural interface.
Full-color single-panel microLED
JBD/Mojo/Saphlux are racing to one RGB panel at high lumens-per-watt — the component that would unlock bright, slim, all-day glasses.
Metasurface & focal-free optics
Flat metasurface lenses and single-layer focal-free designs aim to fix vergence-accommodation and shrink the optical stack — still mostly in academia.
AI-native “glasses without a display”
Ray-Ban Meta shows the assistant can be the product: camera + mic + voice + on-device AI, no waveguide — the fastest-selling category today.
21
AR / HMD PATENT LANDSCAPE

## Slide 22
MIND THE MINEFIELD
IP risk: litigation & freedom-to-operate
Dispute | Subject | Status
Immersion v. Meta | Haptics in Quest | 6 patents; settled w/ license (Feb 2024); 2nd suit on Quest 3.
Mullen v. Meta | VR systems | 12 patents vs. Quest; Meta won a stay pending PTAB review.
Percept v. Magic Leap | AR eyewear | Dismissed with prejudice (Mar 2025) — likely settlement.
IngenioSpec (NPE) | Sensored eyewear | 72-patent portfolio; ITC actions; settled with Meta.
Solos v. Meta + Luxottica | Smart eyewear | 5 patents (Jan 2026); seeks damages “in the multiple billions.”
NPE-led XR litigation is rising; E.D. Texas & the ITC remain favored venues.
Freedom-to-operate watch-list
Clear these (or license) before commercializing waveguide optics:
US 7,457,040 — Lumus reflective waveguide
US 9,372,347 — Microsoft diffractive waveguide
US 9,791,700 — Magic Leap stacked light-field
Apple HMD optics family (US 10,203,489 + continuations)
Also note: foundational optics IP is partly tradeable — licensing is realistic.
Litigation summaries from public dockets & reporting (Bloomberg Law, TechCrunch, court filings). Not legal advice — obtain formal FTO counsel.
22
AR / HMD PATENT LANDSCAPE

## Slide 23
WHAT TO DO WITH THIS
Strategic recommendations for the inventor
1
Aim at the impossible-triangle trade-offs
Concentrate filings on (a) occlusion-capable & selectively-dimming optics, (b) compact low-power varifocal / VAC fixes, (c) high-efficiency full-color microLED + low-eye-glow waveguides. Highest value-per-claim.
2
Stake the input layer early
Meta has a ~238-patent EMG head start. Differentiate on calibration-free generalization, non-wrist biosignals, low-cost EMG, and haptic-confirmed micro-gestures.
3
Own prescription + sub-40 g comfort
Build IP where big-tech portfolios are thin and consumers are unavoidable — Rx-integrated combiners and all-day-comfort ergonomics (the Even Realities / Ray-Ban Display zone).
4
Run FTO before you build optics
Clear or license US 7,457,040 (Lumus), US 9,372,347 (Microsoft), US 9,791,700 (Magic Leap) and Apple’s optics family. Treat foundational optics IP as licensable, not impassable.
5
File US + CN + KR + JP + EP
A US-only filing leaves the fastest-growing market (China, ~56% CAGR) and the display heartland (KR/JP) open. Match the geography to where the market and the supply chain are.
6
Watch the trigger thresholds
Re-prioritize when a shipping device hits >50° FOV at <40 g with all-day battery, or single-panel full-color microLED reaches yield — either event shifts the center of gravity.
23
AR / HMD PATENT LANDSCAPE

## Slide 24
THE BOTTOM LINE
Win the optics and the input — the apps follow.
The AR/HMD patent estate is large, compounding, and concentrated in a handful of optics & display holders. The defensible invention frontier is the hard physics nobody has shipped: hard-edge occlusion, vergence-accommodation, all-day power, prescription optics, and the newly opened neural-input layer. Build a sharp, well-claimed cluster there — in the right jurisdictions — and you are both protected and acquisition-ready.
Patents read: 40+ records examined directly (verified on Google Patents / USPTO) over a synthesized landscape of 140,000+ patents and 67,000+ families.
Sources: LexisNexis IPlytics · GlobalData · Vitek IP · Finnegan · PatSnap · Sagacious IP · IFI Claims · IDC · TrendForce · company filings & primary patent records. Counts vary by methodology; recent years understated by publication lag. Not legal advice — obtain formal FTO/patentability opinions before filing or commercializing.
AR Glasses & Head-Mounted Display Patent Landscape